## Slide 1: Accelerator-level Parallelism Mark D. Hill, Wisconsin & Vijay Janapa Reddi, Harvard @ IISWC/Orlando, November 2019
Aspects of this work on Mobile SoCs and Gables were developed while the authors were “interns” with Google’s Mobile Silicon Group. Thanks!

## Slide 2
Accelerator-level Parallelism Mark D. Hill
University of Wisconsin-Madison
Abstract:
Computer system performance has improved due to creatively using more transistors (Moore’s Law) in parallel via bit-, instruction-, thread-, and data-level parallelism. With the slowing of technology scaling, the only known way to further improve computer system performance under energy constraints is to employ hardware accelerators. Each accelerator is a hardware component that executes a targeted computation class faster and usually with (much) less energy. Already today, many chips in mobile, edge and cloud computing concurrently employ multiple accelerators in what we call accelerator-level parallelism (ALP).
This talk develops our hypothesis that ALP will spread to computer systems more broadly. ALP is a promising way to dramatically improve power-performance to enable broad, future use of deep AI, virtual reality, self-driving cars, etc. To this end, we review past parallelism levels and the ALP already present in mobile systems on a chip (SoCs). We then aid understanding of ALP with the Gables model and charge computer science researchers to develop better ALP “best practices” for: targeting accelerators, managing accelerator concurrency, choreographing inter-accelerator communication, and productively programming accelerators. This joint work with Vijay Janapa Reddi of Harvard. See also: https://www.sigarch.org/accelerator-level-parallelism/
Biography:
Mark D. Hill (http://www.cs.wisc.edu/~markhill) is John P. Morgridge Professor and Gene M. Amdahl Professor of Computer Sciences at the University of Wisconsin-Madison, where he also has a courtesy appointment in Electrical and Computer Engineering. His research interests include parallel-computer system design, memory system design, and computer simulation. He received the 2019 Eckert-Mauchly Award and is a fellow of IEEE and the ACM. He serves as Chair of the Computer Community Consortium (2018-19) and served as Wisconsin Computer Sciences Department Chair 2014-2017. Hill has a PhD in computer science from the University of California, Berkeley.

## Slide 3: Computing Community Consortium (CCC): Catalyzing I.T.’s Virtuous Cycle
Academia
Citizens
Government
Industry
Get involved w/ white papers, workshops, & advocating I.T. research
(to do good & make your research better)
Notes: Established in 2006 as a standing committee of the Computing Research Association
Funded by NSF under a Cooperative Agreement
Facilitates the development of a bold, multi-themed vision for computing research – and communicates this vision to stakeholders
Led by a broad-based Council
Staffed by CRA

## Slide 4: Accelerator-level Parallelism Call to Action
Future apps demand much more computing
Standard tech scaling & architecture NOT sufficient
Mobile SoCs show a promising approach:
ALP = Parallelism among workload components concurrently executing on multiple accelerators (IPs)
Call to action to develop “science” for ubiquitous ALP

## Slide 5: Outline
Computer History & X-level Parallelism
Mobile SoCs as ALP Harbinger
Gables ALP SoC Model
Call to Action for Accelerator-level Parallelism

## Slide 6: 20th Century Information & Communication Technology
Has Changed Our World
<long list omitted>
Required innovations in algorithms, applications, programming languages, … , & system software
Key (invisible) enablers (cost-)performance gains
Semiconductor technology (“Moore’s Law”)
Computer architecture (~80x per Danowitz et al.)
6

## Slide 7: Moore’s Law – 1965 Paper
Optimal number of transistors per chip with increase with time
Became self-fulfilling prophesy with doubling transistor count every ~ two years
Note that transistor gain in two years equals all past gain – the power of an exponential!

## Slide 8
https://www.karlrupp.net/wp-content/uploads/2018/02/42-years-processor-trend.png

## Slide 9: Enablers: Technology + Architecture
  Danowitz et al., CACM 04/2012
Technology
Architecture

## Slide 10: How did Architecture Exploit Moore’s Law?
MORE (& faster) transistors  even faster computers
Memory – transistors in parallel
Vast semiconductor memory (DRAM)
Cache hierarchy for fast memory illusion
Processing – transistors in parallel
Bit-, Instruction-, Thread-, & Data-level Parallelism
Now Accelerator-level Parallelism
10

## Slide 11: X-level Parallelism in Computer Architecture
P
$
M
bus
i/f
dev
1 CPU
BLP+ILP
Bit/Instrn-Level Parallelism

## Slide 12: Bit-level Parallelism (BLP)
Early computers: few switches (transistors)
 compute a result in many steps
E.g., 1 multiplication partial product per cycle
Bit-level parallelism
More transistors  compute more in parallel
E.g., Wallace Tree multiplier (right)
Larger words help: 8b16b32b64b
Important: Easy for software
NEW: Smaller word size, e.g. machine learning inference accelerators
12

## Slide 13: Instruction-level Parallelism (ILP)
13
Processors logically do instructions sequentially (time)
add
Predict direction: target or fall thru
Actually do instructions in parallel  ILP
add
load
branch
and
Speculate!
store
Speculate more!
load
E.g., Intel Skylake has 224-entry reorder buffer w/ 14-19-stage pipeline
Important: Easy for software
IBM Stretch [1961]

## Slide 14: X-level Parallelism in Computer Architecture
P
$
M
bus
i/f
dev
1 CPU
Multiprocessor
BLP+ILP
+ TLP
Thread-Level Parallelism
Bit/Instrn-Level Parallelism

## Slide 15: Thread-level Parallelism (TLP)
Thread-level Parallelism
HW: Multiple sequential processor cores
SW: Each runs asynchronous thread
SW must partition work, synchronize, & manage communication
E.g. pThreads, OpenMP, MPI
On-chip TLP called “multicore” – forced choice
Less easy for software but
More TLP in cloud than desktop  cloud!!
Bifurcation: experts program TLP; others use it
Desk hard + server (cloud) EZ  factor in comp to cloud
Many use few program
Old, Niagara pix
15
Intel Pentium Pro Extreme Edition, early 2000s
CDC 6600, 1964,
(TLP via multithreaded processor)

## Slide 16
https://www.karlrupp.net/wp-content/uploads/2018/02/42-years-processor-trend.png
https://www.nytimes.com/2019/10/07/opinion/ai-research-funding.html

## Slide 17: X-level Parallelism in Computer Architecture
P
$
M
bus
i/f
dev
1 CPU
Multicore
BLP+ILP
+ TLP
Bit/Instrn-Level Parallelism
Thread-Level Parallelism

## Slide 18: Data-level Parallelism (DLP)
Need same operation on many data items
Do with parallelism  DLP
Array of single instruction multiple data (SIMD)
Deep pipelines like Cray vector machines
Intel-like Streaming SIMD Extensions (SSE)
Broad DLP success awaited General-Purpose GPUs
Single Instruction Multiple Thread (SIMT)
SW (CUDA) & libraries (math & ML)
Experimentation as $1-10K not $1-10M
Bifurcation again: experts program SIMT (TLP+DLP); others use it
Pix: cray, cm-5, gpu
18
Illinois ILLIAC IV, 1966
NVIDIA Tesla

## Slide 19: X-level Parallelism in Computer Architecture
P
$
M
bus
i/f
dev
1 CPU
Multicore
GPU
dev-M
Discrete GPU
BLP+ILP
+ TLP
+ DLP
Data-Level Parallelism
Bit/Instrn-Level Parallelism
Thread-Level Parallelism

## Slide 20: X-level Parallelism in Computer Architecture
P
$
M
bus
i/f
dev
1 CPU
Multicore
GPU
Integrated GPU
BLP+ILP
+ TLP
+ DLP
Data-Level Parallelism
Bit/Instrn-Level Parallelism
Thread-Level Parallelism

## Slide 21: X-level Parallelism in Computer Architecture

## Slide 22: Outline
Computer History & X-level Parallelism
Mobile SoCs as ALP Harbinger
Gables ALP SoC Model
Call to Action for Accelerator-level Parallelism

## Slide 23: X-level Parallelism in Computer Architecture
P
$
M
bus
i/f
dev
1 CPU
Multicore
GPU
Integrated GPU
System on a Chip (SoC)
BLP+ILP
+ TLP
+ DLP
Data-Level Parallelism
Bit/Instrn-Level Parallelism
Thread-Level Parallelism
+ ALP
Accelerator-Level Parallelism

## Slide 24: Mobile SoC HW

## Slide 25: Potential for Specialized Accelerators (IPs)
[Brodersen & Meng, 2002]
v
v
16
Encryption
17
Hearing Aid
18
FIR for disk read
19
MPEG Encoder
20
802.11 Baseband
Accelerator is a hardware component that executes a targeted computation class faster & usually with (much) less energy.

## Slide 26: CPU, GPU, xPU (i.e., Accelerators or IPs)
26
2019 Apple A12 w/ 42 accelerators
42 Really?
The Hitchhiker's Guide to the Galaxy?

## Slide 27: Example Usecase (recording 4K video) Janapa Reddi, et al., IEEE Micro, Jan/Feb 2019
ALP = Parallelism among workload components concurrently executing on multiple accelerators (IPs)

## Slide 28: Mobile SoCs Run Usecases
Must run each usecase sufficiently fast -- no need faster
A usecase uses IPs concurrently: more ALP than serial
For each usecase, how much acceleration for each IP?
Accelerators (IPs)  Usecases (rows) | CPUs (AP) | Display | Media Scaler | GPU | Image Signal Proc. | JPEG | Pixel Visual Core | Video Decoder | Video Encoder | Dozens More
Photo Enhancing | X | X |  | X | X | X | X |  |  | 
Video Capture | X | X |  | X | X |  |  |  | X | 
Video Capture HDR | X | X |  | X | X |  |  |  | X | 
Video Playback | X | X | X | X |  |  |  | X |  | 
Image Recognition | X | X | X | X |  |  |  |  |  | 
Notes: Go deeper if time?

## Slide 29: Mobile SoCs Hard To Program For and Select
Envision usecases
(years ahead)
Port to many SoCs??
Diversity hinders use [Facebook, HPCA’19]
What SoC abstraction should SW use?

## Slide 30: Mobile SoCs Hard To Design
Envision usecases (2-3 years ahead)
Select IPs
Size IPs
Design Uncore
Which accelerators? How big? How to even start?

## Slide 31: Outline
Computer History & X-level Parallelism
Mobile SoCs as ALP Harbinger
Gables ALP SoC Model (ok to get lost)
Call to Action for Accelerator-level Parallelism

## Slide 32: Computer Architecture & Models
Multiprocessor & Amdahl’s Law
Multicore & Roofline
Insight
Accuracy
Effort
Models vs Simulation
More insight
Less effort
But less accuracy
Models give first answer, not final answer
Gables extends Roofline  first answer for SoC ALP
Notes: Don’t skip if possible

## Slide 33: Roofline for Multicore Chips, 2009
Multicore HW
Ppeak = peak perf of all cores
Bpeak = peak off-chip bandwidth
Multicore SW
I = operational intensity = #operations/#off-chip-bytes
E.g., 2 ops / 16 bytes  I = 1/8
Output Patt = upper bound on performance attainable

## Slide 34: Roofline for Multicore Chips, 2009
Source: https://commons.wikimedia.org/wiki/File:Example_of_a_naive_Roofline_model.svg
Ppeak
Bpeak* I
(I)
(Patt)
Compute v. Communication: Op. Intensity (I) = #operations / #off-chip bytes

## Slide 35: ALP System on Chip (SoC) Model:
Gables uses Roofline per IP to provide first answer!
SW: optimize for a “gabled roof?”
HW: select & size accelerators
NEW Gables
35
2019 Apple A12 w/ 42 accelerators

## Slide 36: Gables for N IP SoC
A0 = 1
A0*Ppeak
B0
CPUs
IP[0]
← Share off-chip Bpeak →
A1*Ppeak
B1
IP[1]
AN-1*Ppeak
BN-1
IP[N-1]
36
Usecase at each IP[i]
Operational intensity Ii operations/byte
Non-negative work fi (fi’s sum to 1) w/ IPs in parallel

## Slide 37: Example Balanced Design Start w/ Gables
DRAM
IP[0]
CPUs
Bpeak = 10
TWO-IP SoC
IP[1]
GPU
Ppeak = 40
A1*Ppeak = 5*40 = 200
B0 = 6
B1 = 15
Workload (Usecase):
f0 = 1 & f1 = 0
I0 = 8 = good caching
I1 = 0.1 = latency tolerant
Performance?

## Slide 38
Perf limited by IP[0] at I0 = 8
I[1] not used  no roofline
Let’s Assign IP[1] work: f1 = 0  0.75
Ppeak = 40
Bpeak = 10
A1 = 5
B0 = 6
B1 = 15
f1 = 0
I0 = 8
I1 = 0.1
38
Notes: Use these slides rather than website.

## Slide 39
IP[1] present but Perf drops to 1! Why?
I1 = 0.1  memory bottleneck
Enhance Bpeak = 10  30 (at a cost)
Ppeak = 40
Bpeak = 10
A1 = 5
B0 = 6
B1 = 15
f1 = 0.75
I0 = 8
I1 = 0.1
39

## Slide 40
Perf only 2 with IP[1] bottleneck
IP[1] SRAM/reuse I1 = 0.1  8
Reduce overkill Bpeak = 30  20
Ppeak = 40
Bpeak = 30
A1 = 5
B0 = 6
B1 = 15
f1 = 0.75
I0 = 8
I1 = 0.1
40

## Slide 41
Perf = 160 < A*Ppeak = 200
Can you do better?
It’s possible!
Ppeak = 40
Bpeak = 20
A1 = 5
B0 = 6
B1 = 15
f1 = 0.75
I0 = 8
I1 = 8
41
Usecases using K accelerators 
Gables has K+1 rooflines

## Slide 42: μBenchmark w/ Qualcomm SnapdragonTM 835
CPUs GPU DSP (SCALAR)
Ppeak = 7.5 GF AGPU = 47 ADSP-SCALAR = 0.40
All elements load from array & vary FP SP op intensity
Finds empirical lower bound on rooflines
Preliminary evidence that multiple rooflines useful

## Slide 43: Case Study: IT + CAD Vendors (details TBA)
Two cases where: Gables >> Actual
1. Communication between two IP blocks
Root: Too few buffers to cover communication latency
Little’s Law: # outstanding msgs = avg latency * avg BW
https://www.sigarch.org/three-other-models-of-computer-system-performance-part-1/
Solution: Add buffers; actual performance  Gables
2. More complex interaction among IP blocks
Root: Usecase work (task graph) not completely parallel
Solution: No change, but useful double-check

## Slide 44
Into Synopsys design flow << 6 months of publication!

## Slide 47: Case Study: Allocating SRAM
Where SRAM?
Private w/i each IP
Shared resource
SHARED
IP0
IP1
IP2

## Slide 48: What determines Ii?
Hardware
More Ai toward BW-bound (recall fi too!)
More Bi toward compute-bound
More Mi toward compute-bound if reuse
Whither Ii as function of Mi?
SW Usecase (most important)
Dense v. sparse matrices
E.g. vision v. audio ML
Ai*Ppeak
Bi
IP[i]
Mi
Compute -bound Ii
BW -bound Ii
Ii
Patt
48

## Slide 49: Does more IP[i] SRAM help Op. Intensity (Ii)?
Non-linear function that increases when new footprint/working-set fits
Should consider these plots when sizing IP[i] SRAM
Later evaluation can use simulation performance on y-axis
Ii
IP[i] SRAM
Not much fits
Small W/S
fits
Med. W/S fits
Large W/S fits
W/S = working set
49
Compute v. Communication: Op. Intensity (I) = #operations / #off-chip bytes

## Slide 50: Gables Home Page
Model Extensions
Interactive tool
Gables Android Source at GitHub
http://research.cs.wisc.edu/multifacet/gables/

## Slide 51: Mobile System on Chip (SoC)
SW: Map usecase toIP’s w/ many BWs & acceleration
HW: IP[i] under/over-provisioned for BW or acceleration?
Gables is perhaps a first answer, but not a final answer
& Gables
51
2019 Apple A12 w/ 42 accelerators

## Slide 52: Outline
Computer History & X-level Parallelism
Mobile SoCs as ALP Harbinger
Gables ALP SoC Model
Call to Action for Accelerator-level Parallelism

## Slide 53: Future Apps Demand Much More Computing

## Slide 54: Accelerator-level Parallelism Call to Action
Future apps demand much more computing
Standard tech scaling & architecture NOT sufficient
Mobile SoCs show a promising approach:
ALP = Parallelism among workload components concurrently executing on multiple accelerators (IPs)
Call to action to develop “science” for ubiquitous ALP
It’s the SW stupid!
What SW (model) for a gabled-roof SoC?

## Slide 55: X-level Parallel Hardware + Software (Model)
Single-threaded languages, compilers, runtimes, etc. hides parallelism
IBM Power 7
BLP+ILP+TLP
Nvidia GK110
BLP+TLP+DLP
Apple A12
BLP+ILP+TLP+DLP+ALP
Intel Pentium Pro
BLP+ILP
Software abstracts TLP, e.g., pThreads, OpenMP, & MPI.
Also hidden in cloud, etc.
Software abstracts TLP+DLP, e.g., CUDA, OpenCL, & graphics OpenGL
Also hidden in cloud, etc.
Local software stack abstracts each accelerator.
But no good, general software abstraction for SoC ALP!
Notes: Pentium Pro ca. 1995+ 5M transistors

## Slide 56: ALP/SoC Software Descent to Hellfire!
Hellfire!
P P P P
P P P P
P P P P
P P P P
Heterogeneous
Multicore
Thought bridge: Must divide work heterogeneously
P P P P
P P P P
P P P P
P P P P
Homogeneous
Multicore
Any thread-level parallelism, e.g., homogeneous
P P D E
A A C C
A A C C
A B B B
Heterogeneous
Accelerators
Accelerate each differently with unique HLLs (DSLs) & SDKs
P P D E
A A C C
A A C C
A B B B
Today: Device
Accelerators
All of above & hide in many kernel drivers 
P
Uniprocessor
No visible parallelism
Key: P == processor core; A-E == accelerators
Local SW stack abstracts each accelerator.
But no good, general SW abstraction for SoC ALP!
Notes: Pentium Pro ca. 1995+ 5M transistors

## Slide 57: SW+HW Lessons from GP-GPUs?
Nvidia GK110
BLP+TLP+DLP
Feature | Then | Now
1. Programming | Graphics OpenGL | SIMT (Cuda/OpenCL/HIP)
2. Concurrency | Either CPU or GPU only; Intra-GPU mechanisms | Finer-grain interaction Intra-GPU mechanisms
3. Communication | Copy data between host & device memories | Maybe shared memory, sometimes coherence
4. Design | Driven by graphics only; GP: $0B market | GP major player, e.g., deep neural networks
Programming for data-level parallelism: four decades SIMDVectorsSSESIMT!

## Slide 58: SW+HW Directions for ALP?
Feature | Now | Future?
1. Programming | Local: Per-IP DSL & SDK Global: Ad hoc | Abstract ALP/SoC like SIMT does for GP-GPUs
2. Concurrency | Ad hoc | GP-GPU-like scheduling? Virtualize/partition IP?
3. Communication | SW: Up/down OS stack HW: Via off-chip memory | SW+HW for queue pairs? Want control/data planes
4. Design, e.g., select, combine, & size IPs | Ad hoc | Make a “science.” Speed with tools/frameworks
Apple A12: BLP+ILP+TLP+DLP+ALP
Need programmability for broad success!!!!
In less than four decades?

## Slide 59: Challenges
Programmability
4. Design Space
3. Communication
2. Concurrency
Whither global model/runtime?
Best HW-assist for fine-grain scheduling?
How should SW stack reason about memory, caches, queues, & scratchpads?
When combine “similar” accelerators?
Opportunities
    Hennessy & Patterson: A New Golden Age for Computer Architecture
Science

## Slide 60: #1: Accelerator Design Space
What is the “right” set of accelerators? For HW? For SW?
When should “similar” accelerators be combined?
When should accelerators share resources (e.g., SRAM)?
How to future-proof for change (e.g., machine learning)?
How should tools/frameworks speed accelerator design?

## Slide 61: #2: Accelerator Concurrency
How to cooperatively schedule accelerators? By OS or runtime? As devices or processor peers? What HW mechanisms? Note: GPU tasks use runtime & HW
Policies/mechanisms manage/partition/virtualize shared resources (compute, cache/memory, interconnect)?
Whither OS/runtime Hardware Abstraction Layer (HAL)? What should HALs hide/expose?

## Slide 62: #3: Accelerator Communication
How do accelerators communicate data? Through memory, shared cache, queues, scratchpads? #copies? Abstraction(s)? Stream dataflow? Idempotent (RDDs)?
Note: GPU memory: discretesharedcoherent
How do accelerators communicate control? Through interrupts or polling (both bad) Via CPUs? Other?
Separate or unified drivers?

## Slide 63: #4: Accelerator Programmability
Each accelerator has domain-specific language (DSL) w/ SDK, JIT, runtime, etc.? Phone  more generally?
Unify multiple accelerator SW “stacks” somehow?
Tools/frameworks to speed SW development? “SW is behind HW” true since 1940s if new SW required
#1-4 needed to delivery ubiquitous ALP to future apps!
Do for ALP what SIMT/runtimes did for GPU TLP+DLP!

## Slide 64: Picking Research Problems & ALP
Look for change – gives fresh opportunity
 ALP applications, software, & hardware will explode
2. If you can do it, people will care
3. You can do
(some of) it
 True for general ALP
Must answer for yourself!

## Slide 65: Accelerator-level Parallelism Call to Action
Future apps demand much more computing
Standard tech scaling & architecture NOT sufficient
Mobile SoCs show most/only promising approach:
ALP = Parallelism among workload components concurrently executing on multiple accelerators (IPs)
Call to action to develop “science” for ubiquitous ALP
    Hennessy & Patterson: A New Golden Age for Computer Architecture
Science

## Slide 66: Backup Slides

## Slide 67: Computing Community Consortium
The mission of Computing Research Association's Computing Community Consortium (CCC) is to catalyze the computing research community and enable the pursuit of innovative, high-impact research.
Who
Council ~24 members
CCC/CRA Staff
Chair, VC, & Director
Inputs: Bottom-up, Internal, & Top-Down
What:
Workshops & Conf. Blue Sky Tracks
Whitepapers & Social Media
Reports Out (esp. to government)
Biannual Symposium to DCers
Human Development
Early Career Workshops & Participation
Council Membership
Leadership w/ Gov’t (LISPI)
point successes, lacking SW/HW science
point successes, lacking SW/HW science
Notes: Established in 2006 as a standing committee of the Computing Research Association
Funded by NSF under a Cooperative Agreement
Facilitates the development of a bold, multi-themed vision for computing research – and communicates this vision to stakeholders
Led by a broad-based Council
Staffed by CRA

## Slide 68: A Parallelism Lattice

## Slide 69
IPs should target important workloads, but …
Pitfall X: Design for (Hyped) Importance
Recommend: Provision IP resources (compute & SRAM) only as needed for important usecases
Gartner

## Slide 70: Gables Math: Roofline / Work Fraction
Roofline: MIN(Bpeak * I, Ppeak)
MIN(Bpeak * I, 1 * Ppeak) / 1
1 / TIP[i] = MIN(Bi * Ii, Ai * Ppeak) / fi fi ≠ 0
1 / Tmemory = Bpeak * Iavg Iavg = 1 / Σi=1,N-1(fi / Ii)
Perf = MIN(1/TIP[0] , …1/TIP[N-1], 1/Tmemory)
70